## Slide 1: Fan Speed PID Controller using Analog Components
Names: I.Ds:
Marwan sultan 21-101138
Tamer Ahmed 21-101103
Mohamed Ehab 21-101110
Ahmed Daib 21-101102
Porf.Nader Madkor

## Slide 2: Introduction
PID controllers are fundamental in control systems.
Project aim: implement analog PID for fan control.
Three-stage methodology: digital, simulation, hardware.
Target: control fan speed using only analog components.

## Slide 3: System Overview
Closed-loop PID control system for 12V DC fan.
Main blocks: Setpoint input, Tachometer Feedback, F-V Converter.
Instrumentation Amplifier, PID Controller, Output Stage.
Power: Dual ±24V supplies for op-amps.

## Slide 4: Phase I: Digital Prototyping
Used microcontroller to prototype control logic.
Tuned PID parameters via Ziegler–Nichols method.
PWM to analog via RC filter, amplified to 12V.
Built baseline understanding of system behavior.

## Slide 5: Phase II: Analog Simulation
Simulated analog PID in Multisim 14.3.
Built op-amp based integrator, differentiator, gain blocks.
F–V conversion using LM2907N IC.
Simulated real-world behavior of tachometer feedback.

## Slide 6: Phase III: Hardware Implementation
Built full circuit using breadboard and op-amps.
Used potentiometers for tuning PID gains.
Overcame power supply challenges (dual ±24V).
Kick-start mechanism added for 0-RPM deadlock.

## Slide 7: Experiments & Results
Digital phase: effective PWM control with PID tuning.
Simulation: convergence achieved, validated design.
Hardware: stable control, disturbance rejection.
Minor issues (e.g., zero feedback at rest) resolved.

## Slide 8: Challenges & Fixes
Signal instability solved using pull-up resistors and diodes.
Power delivery improved via Darlington transistors.
Feedback loss at 0 RPM resolved with manual pulse.
Fine-tuning needed due to real-world non-idealities.

## Slide 9: Future Work
Adaptive PID with real-time tuning.
Single-supply design using rail-to-rail op-amps.
Smaller F–V transducers or PLL-based feedback.
Hybrid analog-digital systems for monitoring.

## Slide 10: Conclusion
Successfully implemented analog PID for fan speed control.
Phased approach ensured systematic learning.
Project bridged theoretical knowledge with hardware design.
Useful for educational and low-cost control applications.

## Slide 11: Acknowledgments
Prof. Nader Mansour – project guidance and flexibility.
Dr. Mohammed Anwar – lab equipment support.
Team collaboration and iterative development were key.

## Slide 12
Thank you.
Any questions.